## Slide 1: NorthBound Infrastructure Centralised Management Daemon (CMGD) Design Discussions
Pushpasis Sarkar spushpasis@vmware.com

## Slide 2: Agenda – 2021/09/13
CMGD to be renamed to MGMTD
Update on Scale handling
  Issue with nb_validate_yang() and nb_config_diff()
  Scratch buffer of uncommitted commands.
  Offline processing of Config apply on Back-end – Revert Back
    Need to implement PREPARE_REQ instead.
  Vtysh –f handling
Handling of VTYSH commands
  Decide where to load and run the command handlers
  Implicit commit for config commands from VTYSH in regular mode.
    Need to still figure out how to utilise ‘cmgd commit-apply’ from VTYSH.
Handling rollback of configuration.
  Upto 10 last commit buffers to be saved.
  Offline job for saving commit buffers to file on disk.

## Slide 3: Progress on Scale so far
Test scale with 10k static routes
  On master
    With ‘vtysh –f’ takes 7 seconds
  On yang_cmd_dev
    With ‘vtysh –f’
      Set-Config takes 3.6 seconds
      Commit takes 1.4 seconds
      Total: 6 seconds.
    With ‘cmgd load-config’
      Load-Config takes 1-2 seconds
      Commit takes 1.4 seconds
      Total: 3.5-4 seconds.

## Slide 4: Applying configurations on Backend

## Slide 5: Applying Config on Backend
Config is pre-validated on CMGD.
  No need to wait for APPLY on Backend for Commit to complete.
CFG_APPLY_REQ is queued for processing later.
  Pros
    Commit can return much earlier.
    Configuration apply can be spread over time to let other job on the same thread.
    Or can be packed into a much lesser batches than what was possible with inline processing.
  Cons
    If and only if apply fails, the backend becomes out-of-sync with Config on CMGD.
    How to recover?
      Perhaps restart the backend daemon and re-download config on restart. ???
Offline processing of CFR_APPLY_REQ

## Slide 6: Handling VTYSH commands

## Slide 7: Current Method
Current Config Commands Processing
Staticd
VTYSH
Zebra
lib/vty.c
static_vty.c
static_nb_
config.c
lib/vty.c
zebra_vty.c
zserv.c
X
show ip route
show running config
ip route x.x.x.x/y
X

## Slide 8: Option 1
CMGD
Frontend
Adapter
Backend
Adapter
lib/vty.c
Transactions
Running
DB
Candidate
DB
FE
static_vty.c
bgp_vty.c
Diverted to and Processed on CMGD
Staticd
VTYSH
BGP
lib/vty.c
static_vty.c
static_nb_
config.c
Backend
Client Lib
lib/vty.c
bgp_vty.c
X
router bgp 100
CMGD config and show commands
ip route x.x.x.x/y
ip route x.x.x.x/y
X
SET_CONFIG
<xpath, value
CREATE_DATA
<xpath, value>
VALIDATE_REQ
APPLY_REQ
cmgd commit-apply
COMMIT-CONFIG
bgp_nb_
config.c
X
Backend
Client Lib
CREATE_DATA
<xpath, value>
VALIDATE_REQ
APPLY_REQ
router bgp 100
X

## Slide 9: Option 1
Command handlers lib-ified and loaded on CMGD
  Cannot access any internal state of the Back-end application daemon.
  Passes set of Xpaths, values and operations to CMGD Front-end connection.
Pros
  Single connection from VTYSH to CMGD (and not multiple backend daemons).
  Conversion from string commands to Xpaths/Value/Operation is no more a computational burden on the back-end application daemon.
Cons
  Auto-completion cannot be done as is today.
    Needs to fetch data from Back-end and then present auto-completion options.
Diverted to and Processed on CMGD

## Slide 10: Option 2
CMGD
Frontend
Adapter
Backend
Adapter
lib/vty.c
cmgd_vty.c
Transactions
Running
DB
Candidate
DB
Retained and processed on Backend daemon
VTYSH
CMGD config and show commands
SET_CONFIG
<xpath, value
CREATE_DATA
<xpath, value>
VALIDATE_REQ
APPLY_REQ
cmgd commit-apply
COMMIT-CONFIG
Staticd
BGP
lib/vty.c
static_vty.c
static_nb_
config.c
Backend
Client Lib
lib/vty.c
bgp_vty.c
X
router bgp 100
ip route x.x.x.x/y
bgp_nb_
config.c
X
Backend
Client Lib
CREATE_DATA
<xpath, value>
VALIDATE_REQ
APPLY_REQ
FE
FE
COMMIT-CONFIG

## Slide 11: Option 2
Command handlers running on Back-end daemons as is today
  Can access any internal state of the Back-end application daemon.
  Passes set of Xpaths, values and operations to CMGD Front-end connection.
Pros
  Auto-completion can be done as is today.
Cons
  Conversion from string commands to Xpaths/Value/Operation is still a burden on the back-end application daemon.
  VTYSH continues to maintain connections to all individual back-end application daemons.
Retained and processed on Backend daemon

## Slide 12: THANK YOU!!!